DCCDIP1 race - color, position wires

| color in cable adapter | pin no. in connector | name | description |
| --- | --- | --- | --- |
| grey/black | 1 | INPUT 3 | multifunction input |
| white/black | 2 | POT | correction potentiometer (analog input) |
| green/yellow | 3 | TACHO | tachometer output |
| blue | 4 | COM GND | ground for RS232 (pin 5 in 9pin connector) |
| red | 5 | SUPPLY +12V | supply +12 V |
| violet | 6 | POWER OUT 1 | power out 1 (fuel pump relay) |
| blue/white | 7 | POWER OUT 2 | power out 2 (gear shift light) |
| pink | 8 | POWER OUT 3 | power out 3 (POWER JET Honda) |
| orange | 9 | IC (ignition coil) | ignition coil |
| blue | 10 | GND | power ground |
|  | 11 | NC | not connected |
| black | 12 | INPUT 2 | multifunction input 2 |
| green/orange | 13 | kill switch | not maskable kill switch |
| red/black | 14 | AC SUPPLY | main ac supply |
| red/black | 15 | AC SUPPLY | main ac supply |
|  | 16 | NC | not connected |
| yellow/black | 17 | AC SUPPLY | auxiliary ac supply |
|  | 18 | NC | not connected /TWS |
| grey/red | 19 | INPUT 1 | multifunction input 1 |
|  | 20 | NC | not connected |
| white/red | 21 | + 5V | supply +5V for sensors |
| black | 22 | COM | RS232 (pin 2 in 9pin connector) |
| yellow | 23 | COM | RS232 (pin 3 in 9pin connector) |
| violet | 24 | COM | RS232 connector (pin 1 in 9pin connector) |
| orange | 25 | COM | RS232 connector (pin 9 in 9pin connector) |
| blue | 26 | SENSE GND | ground for pickup |
| yellow | 27 | PICK-UP | pickup |
| white/red | 28 | + 5V | supply +5V for sensors |
| grey | 29 | TPS | throttle position sensor input |
| blue | 30 | SENSE GND | ground for sensors |
| white/blue | 31 | STPS | servomotor position sensor input |
| green | 32 | M+ | output for servomotor |
| green | 33 | M- | output for servomotor |
|  | 34 | NC | not connected |